## Slide 1
Bio-Inspired High Speed Pupil-Tracking using a Dynamic Vision Sensor
Joseph Warren, Yufei Wu, Aldo Faisal

## Slide 2: Algorithmic Framework
Pupil Position (x,y)

## Slide 3: Network Architecture & Data
~40000
5
5
5x5 groups
10 neurons/group

## Slide 4: Learning Rules for Feature Extraction
STDP
  Creates selectivity to spatio-temporal patterns
Lateral Inhibition
  Leads to competition between neurons
Dan Y, Poo MM. Spike timing-dependent plasticity of neural circuits. Neuron. 2004; 30;44(1):23-30

## Slide 5: Results
Neuron ID
Receptive Fields for 10 neurons covering 5x5 patch

## Slide 6: (Bad) Feature Extraction at Higher Layers…
Problem: learning is happening at higher levels, but learning from poor features…
Layer 1 (5x5)
Layer 2 (4x4)
Layer 3 (3x3)

## Slide 7: Solution: Fix bottom layer
Bottom layer is not extracting good features
  Limits ability of higher layers
Enlarge Receptive Fields of neurons
  5x5 to 16x16
  Features not present at lower scales
Initialise receptive fields of neurons prior to learning
  How to find ideal receptive fields to initialise with?
    Sparse coding

## Slide 8: Sparse Coding
Finds ‘dictionary’ of features that best represent data
Features are such that each data sample is a sparse combination of features in dictionary
  i.e. want to use few features per sample
This can be used to find receptive fields!
  Has been used for natural images
  Need to repeat for DVS data (i.e. event data)

## Slide 9: Sparse Coding results from DVS data
Strong orientation selectivity
  In agreement with receptive fields of visual cortex
Conclusion: initialise neurons as orientation-selective
  Each neuron has preferred angle

## Slide 10: Detour to Biology
Orientation-selective cells
End-capped orientation-selective cells
Hubel, D. (1988). Eye, Brain, and Vision. 1st ed. New York: Scientific American Library.

## Slide 11: Final Solution
Going to initialise first layer weights
Incorporate two categories
  Orientation-selective
  End-capped orientation-selective
Test selectivity
  Made synthetic data:
    Moving bar
    Moving circle of variable radius
Preferred Angle:
45o
0o
Preferred radius of curvature:
10 pixels
Inf (straight)

## Slide 12: Data collection
Installed IR light source
  Shows pupil better
  Below safe limit (10mW/cm2)
For each frame we need pupil position (x,y) for reward
  Use standard pupil detector/hand labelling
Protocol for training data
  Even distribution of pupil positions?
  Random eye movement?
  Different sittings
Test data
  Random (natural) eye movement
  Different time of day?
  Different eye-position?
  Different user?

## Slide 13: Reward Layer
Population code
  Effectively classification
Each neuron corresponds to pupil position
  (x,y) in pixels
Reward conveyed via synaptic potentiation or depression
Don’t want one-hot classification
  Some wrong predictions are better than others
Need to deal with asynchrony between reward time and prediction time

## Slide 14: Plan for next month
After 1-1.5 weeks
  Feature extractor finished
    Tested with synthetic data, selectivity proven
  Data collected and labelled
After 2.5-3 weeks
  Reward layer working
  Accuracy & latency measured
After 4 weeks
  High-speed performance verified on lab computer
  Report